## Slide 1: Student Laboratory Safety Training
College of Science, Technology, Engineering and Mathematics

## Slide 2: Hazard Communication
The Occupational Health & Safety Administration (OSHA) regulates workplace safety
  Hazard Communication Standard (HazCom) is for workplaces with hazardous chemicals
HazCom training must include information on:
  Hazardous Chemical Exposure
  Hazard detection
  Measures of protection
  Chemical labels & Safety Data Sheets (SDSs)
Notes: OSHA regulates workplace safety in the private sector. The HazCom Standard was developed to provide protection and information to employees in workplaces with hazardous chemicals and requires training for employees.
Training on HazCom elements is provided to student employees, researchers, and volunteers working in the labs outside of their general course work. Training involves information on hazardous chemical exposure, detection and protection. It also includes information on chemical labeling and SDSs.

## Slide 3: Responsibility
Lock doors whenever room is vacated
Do not unlock door for others
Access is restricted to normal University hours (7am – 10pm)
Supervisor must be within building to assume responsibility
Student activity within lab/room must be within scope of work as defined by supervisor
Do not use equipment, instruments, tools, etc. without permission.
Follow all safety guidelines for each piece of equipment, instrument, tool, etc.
If unsure how to run equipment, instruments, tools, etc. – Ask!
Return equipment, chemicals, supplies, etc. to correct storage location.
Maintain a safe and clean work space

## Slide 4: Loss of Privilege/Access
Dean provides all access privileges and has right to revoke privileges
Actions resulting in loss of privilege:
  Damaged equipment, room or furniture
  Unsafe acts – putting others at risk
  Unsupervised before/after-hour use
Can result in faculty sponsor’s ability to provide access to other students

## Slide 5: Onity Lock Operation
Most Onity locks require Onity key cards to be dipped once to unlock and dipped again w/ door in the closed position to lock.
Green = Unlocked, Red = Locked
If you exit through a door that was locked, you have unlocked that door. Do not leave without ensuring all doors are locked.
Report problems to supervisor/faculty member.
Notes: Onity locks keep room access logs, so if something were to happen, the log may be referenced to determine who may have been involved or have knowledge. It is important to ensure that you lock labs upon leaving. Understand how the locks to the rooms that you will be accessing work so that you know that you are securing labs when leaving (some lock automatically, some do not). It is recommended that if you unlocked a lab, you lock that lab upon leaving even when others entered the unlocked lab after you. This will ensure that you have a “time stamp” of when you entered and left the lab and you won’t lock others in the room.

## Slide 6: General Lab Safety
No eating or drinking in any lab
Always wear appropriate PPE as directed
Never wear shorts or open-toed shoes
Avoid loose fitting clothing & long jewelry
No unauthorized “experiments” in the lab
Clean-up small spills immediately, report large spills to supervisor/faculty member
All near-misses and injuries should be reported

## Slide 7: Emergency Procedures
Call 911 (9-911 from Red Phones & SU land lines)
  Fire, serious bodily injury
Non-Emergency Call Boxes
  Push to talk, release to listen
  Connect directly to Facilities
  Located in:
    Byrd Science Center NE corridors
    Snyder Hall corridors
    Stutzman-Slonaker Hall corridors
Non-emergency events – inform faculty member or use chain of contacts (next to doors leading to each lab)

## Slide 8: Emergency Equipment
Most laboratories have the following emergency equipment
  Eye Wash Stations
  First Aid Kits
  Spill Kits
  Showers
  Emergency Gas Shutoffs
  Fire Extinguisher
  Fire Blanket
Notes: Take note of the location of emergency equipment in the labs in which you will be working. Most labs are laid out in a similar fashion, but there are minor differences.
Fire extinguisher use: Use the PASS method (Pull the pin, AIM the nozzle at base of fire, SQUEEZE the handle, SWEEP side to side)
Fire blankets can be used to put out small fires.

## Slide 9: Hierarchy of Hazard Controls
Notes: There are different methods of controlling hazards in order to protect yourself. Understanding how hazards are and can be controlled is important in ensuring your own safety. OSHA, CDC and other health and safety organizations and regulatory agencies use a Hierarchy of Controls that can be used to provide protection from hazards.
The first step is to always see if a hazard can be eliminated (e.g. removing a highly toxic chemical from a lab experiment). If a hazard cannot be eliminated, can it be substituted for something less hazardous? (e.g. replacing a highly toxic chemical with a chemical with a low toxicity to achieve the same results).
The second step is to use engineering controls provided. For instance, use of chemical fume hood helps provide protection from harmful vapors. Engineering controls require a change to the workplace and can expensive.
The third step is to utilize administrative controls. These include things such as policies, training, and housekeeping. This requires your participation!
Lastly, PPE, such as gloves, goggles an lab coats, is considered. As the last line of defense, PPE is an important component of lab safety!

## Slide 10: Engineering Controls
Remove or provide a barrier from hazard such as:
  Chemical fume hood
  Biosafety cabinet (BSC)
  Machine guard
  General HVAC
Notes: General HVAC and Chemical fume hoods are the most common engineering controls in labs. General HVAC ensures fresh air is continuously introduced into the lab and is not recirculated. Chemical fume hoods provide additional protection when working with hazardous chemicals. Machine guards and biosafety cabinets are other engineering controls that may be seen in SNS&M labs.

## Slide 11: Administrative Controls
Require action – rely on users
  Training
  Policy/Procedures
  Housekeeping & Hand washing
  Preventative Maintenance
Notes: The training that students go through for access approval and the policy that requires the training are both examples of administrative controls. Employer/supervisor and employee/student are both required to take part. Labeling chemical and waste containers and ensuring containers are closed, housekeeping and hand washing and preventative maintenance and testing/calibrating equipment are all examples of administrative controls.

## Slide 12: Personal Protective Equipment
Least effective control
  Gloves
  Goggles
  Lab Coats
  Closed-toed Shoes
  Face Shields
(Wear appropriate size)
Notes: The least effective control (and last control to consider) is PPE. PPE requires the employee/student to do something (don/doff goggles, gloves, etc.). Other controls can be in place to minimize exposure to a hazard, but a potential exposure still exists. PPE provides protection from expected or incidental hazard exposures. Just because other controls are in place, it does not mean that PPE is optional! For example, just because you are working in a hood with a solvent does not mean that goggles and gloves should not be worn.

## Slide 13: Electrical Safety
Damaged or loose electrical cords should be replaced or repaired – do not use them!
  Report these to your supervisor/faculty member.
Extension cords are for temporary use. Avoid running them across aisles and doorways
Avoid overloading outlets.
Do not daisy-chain/piggyback power strips or extension cords.
Check all cords prior to use!

## Slide 14: Piped Gas Safety
Ensure all gas valves are in the closed position prior to use
Connect device (inspect device and tubing)
Make appropriate adjustments to device
Open emergency gas valve (if in the off position)
Follow applicable procedures for use of device
When finished, close benchtop valve
Ensure emergency gas valve is off (Push to stop)
Notes: Check emergency gas valve to ensure it is in the “off” position (pushed down). Prior to use, ensure that all valves are in off position. Connect device and inspect device and tubing for defects – do not use faulty tubing or devices! If applicable, make appropriate adjustments to device. Open the emergency gas valve. Turn on gas valve connected to device at benchtop. Follow applicable procedures for proper use of connected device. When finished, close the benchtop valve (handle perpendicular to gas line). Check to ensure all other valves are closed. Turn off gas at emergency gas shutoff (push down).

## Slide 15: Chemical Fume Hood Safety
Provide protection from hazardous and toxic chemicals
  Does not exempt user from wearing required PPE
  Ensure sash is at proper operating level
  Work should be performed six inches from plane
  Do not cross plane of hood opening w/ head
  Close sash when not in use

## Slide 16: Chemical Routes of Entry
Ingestion
  through the digestive tract
Absorption
  through the eyes, skin or mucous membranes
Inhalation
  through the respiratory tract
Injection
  piercing the skin
Protect yourself from exposure!
Notes: You will be working in a lab, so it is important to understand how you can be exposed and how to protect yourself from exposure. There are four routes of entry – Ingestion, Absorption, Inhalation and Injection. Knowing the potential routes of entry is important in identifying the controls that can be used to protect yourself from exposure.

## Slide 17: Methods of Detection
Protect yourself by using your senses!
Recognize when hazards may be present
Examples:
  Smell odorant in propane, burning material or chemical
  See a spill, bulging container, uncapped needle
  Hear the hissing of a container or gas cylinder
  Hear an alarm beeping or buzzing
  Feel dizzy or light-headed
  Feel burning sensation of skin
Notes: Protect yourself by using your senses to recognize when hazards may be present. Smelling, seeing, hearing, feeling or even tasting something can indicate that you have been or are being exposed to a hazard. Report all hazards observed or perceived immediately to your supervisor.

## Slide 18: Labeling: Primary Containers
Name, Address and Telephone Number
Signal Word (“Danger” or “Warning”)
Hazard Statements
Precautionary Statements (4)
  Prevention, Response, Storage, Disposal
Pictograms (9)
Supplementary Info (not required)
Notes: Chemical labeling is a requirement. It is an important administrative control. Without labeling, human and environmental health can be put at risk. HazCom requires

## Slide 19: Pictogram Hazards
Notes: There are four health hazard pictograms: 1. Health Hazard; 2. Exclamation Mark; 3. Corrosion; 4. Skull & Crossbones
There are five physical hazard pictograms: 1. Flame; 2. Gas Cylinder; 3. Corrosion; 4. Exploding bomb; 5. Flame Over Circle
There is one environmental hazard pictogram: 1. Environment

## Slide 20: Labeling: Secondary Containers
All containers, except those for immediate use, must be labeled
At minimum, must include:
  Product Identifier/Chemical Name (no abbreviations, no chemical formulas, etc.) AND
  Product/Chemical Hazards (Words, symbols or combination of words and symbols)

## Slide 21: NFPA Label
National Fire Protection Association (NFPA) 704 Hazard Rating System
  Ratings are 0 (no hazard) to 4 (severe hazard)
  Health (Blue); Flammability (Red); Instability (Yellow); Special Hazard (White) 6 o’clock
  Position always the same
    Health 9 o’clock
    Flammability, 12 o’clock
    Instability, 3 o’clock
    Special hazard, 6 o’clock
  May be in black and white

## Slide 22: Safety Data Sheets
Provide information on hazardous chemicals
Must be accessible to employees (including student employees) for each hazardous chemical in the workplace
Students and employees may access SDSs in:
  Most labs and/or prep rooms (binder)
  Online at www.shepherd.edu/safety
  Online by searching a vendor’s website
  3E Company 1-800-451-8346

## Slide 23: SDS Sections
Identification
Hazard(s) Identification
Composition/Information on Ingredients
First-aid Measures
Fire-fighting Measures
Accidental Release Measures
Handling and Storage
Exposure Controls/Personal Protection
Physical and Chemical Properties
Stability and Reactivity
Toxicological Information
Ecological Information
Disposal Considerations
Transport Information
Regulatory Information
Other Information
  Jones Reagent SDS

## Slide 24: Bio-hazardous Waste
Waste placed in containers includes:
  Cultures and stocks of toxic agents;
  Human & non-human blood, body fluids & tissue;
  Products contaminated with blood/tissue or other potentially infectious materials;
  Contaminated glass and plastic (pipettes, Petri dishes, etc.)
DO NOT place contaminated items in the general waste.
DO NOT place general waste in Bio-Waste Boxes
DO NOT overfill Bio-hazardous containers or sharps containers – request new containers from your supervisor or visit BY208.
When in doubt, ask!

## Slide 25: Bio-hazardous Waste
Dispose of biological waste in the bio-hazardous waste containers, sharps in sharps containers.
Extra supplies (boxes, liners, sharps containers) may be requested in BY208.
Bio-hazardous containers and sharps containers are located in:
  BY203
  BY204
  BY210
  BY211
  SS306
  SS303

## Slide 26: Hazardous and Chemical Waste
Cradle-to-Grave requirement to manage all hazardous waste
All hazardous waste must be identified and labeled
Common laboratory hazardous wastes:
  Corrosive/Caustic liquid wastes
  Flammable wastes (Flash point < 140°F)
  Reactive wastes
  Toxic wastes
    Heavy metal wastes (Arsenic, Barium, Cadmium, Chromium, Lead, Mercury, Selenium, Silver)
    Certain organic chemicals (Benzene, Carbon tetrachloride, Chloroform, Cresols, Methyl ethyl ketone, Nitrobenzene, Pyridine)
    Certain pesticides
Notes: Shepherd University has a cradle-to-grave management requirement for all hazardous waste it generates under EPA and WV DEP regulations.
Typical wastes generated in the SNS&M labs are those that are corrosive, ignitable/flammable (including oxidizers), reactive and toxic.
Toxic

## Slide 27: Hazardous and Chemical Waste
Consult your supervisor/sponsoring faculty member before disposing of any waste.
Read the labels!
Do not mix incompatible wastes
Do not fill containers completely – leave room in neck of containers or leave 1in. From top of wide mouth containers
All containers of hazardous waste must be closed, except when adding or removing waste
If unsure – ask!
Notes: ALWAYS READ THE LABELS BEFORE ADDING WASTE TO A CONTAINER. WHEN IN DOUBT, ASK! Filling containers completely, especially with incompatible wastes can be dangerous. Always keep containers closed, except when adding or removing a waste (EPA and WV DEP requirement).

## Slide 28: Hazardous Waste Labeling
All hazardous waste must be properly labeled with:
  The words “Hazardous Waste”
  All Contents*
    Abbreviations, chemical formulas and other forms of short hand are not allowed
  The Accumulation Start Date
Notes: A pre-printed hazardous waste label is not required, but can make labeling easier. Ensure that the three required elements are on container even if no pre-printed label is available. Ensures safety when handling and disposing or recycling. Think of those down stream! Must know when something is generated for compliance purposes.

## Slide 29: Generator Responsibility
Step 1
Waste Determination
Step 2
Container Selection
Step 3
Containerize Waste
Step 4
Label Container
Step 5
Container Management
Notes: Determine if it is a hazardous waste - consult supervisor or instructor.

## Slide 30: Do not mix incompatible wastes!
Notes: Dangerous situations when filling containers completely (no room in neck of container) and mixing incompatibles (conc. Acid and conc. Base). Better to start a new container of waste than chance an unwanted reaction.

## Slide 31: Questions?